## Slide 1
Vector Extension for Wireless Signal Processing base on RVV 1.0
05/2024
ligaoshan@cmiot.chinamobile.com

## Slide 2
RISC-V RVV 1.0 Advantages
eliminates licensing,reduced costs,broader adoption,leading to faster innovation
Open Standard
1
single instruction process much more data, leading memory access and power efficiency
Efficiency
3
scale vector lengths without changing the core arch.
from low-power embedded systems to high-performance
Scalability and Flexibility
2
simplifies programming, compiler design and micro-arch design
Orthogonality
4
RVV
Notes: 字体要求：微软雅黑 12-18号字体
具体内容、文字及图表要求不限（可展开多页）

## Slide 3
RISC-V V is efficient
Micro-Arch Opt is easy
pipeline between multi-VR operation is possible
Reduce Loop
single instruction can process multiple VR
B
C
A
Reduce codesize
data longer than VLEN can be processed naturaly
Compared to traditional SIMD (etc. ARM Neon , x86 SSE/AVX)，difference is VLEN is a variable
Notes: 字体要求：微软雅黑 12-18号字体
具体内容、文字及图表要求不限（可展开多页）

## Slide 4
Wireless Signal Processing has additional ISA requirements
Chart: RVV application scenarios
| ML&AI | Sci. | DSP | Cryp | Graph | MM
系列 2 | 0.3 | 0.2 | 0.08 | 0.12 | 0.1 | 0.2
RVV not mature for DSP
Over 50% application for AI & Grap
block wise stride load/store,
float point vector instruction,
common nonlinear function, rsqrt, recip
etc.
Wireless DSP still need:
Dynamic scaling to fully utilize the dynamic range&accuracy with limited bitwidth
Complex number related instructions
highly efficient non-linear functions
highly efficient inter-element instructions
Notes: 字体要求：微软雅黑 12-18号字体
具体内容、文字及图表要求不限（可展开多页）

## Slide 5
“Zvw” Extention overview, W for Wireless
aaa
Complex number inst.
>20 complex related vector instruction
01
aaa
Dynamic Scaling for multiply & accu.
>20 dynamic scaling functions
02
aaa
fast Non-linear inst.
3 unified fast non-linear functions
03
aaa
Efficient Inter-element Inst.
>3 Perm. + funnel shift instrutions
04
aaa
Sequence generation Inst.
several sequence Gen instructions
05

## Slide 6
Typical Key instructions
vconj(vector complex conjugate)
vcpack(vector complex packing instruction)
vcunpack(vector complex packing instruction)
vdscmul (vector dynamic scaling complex multiply)
vdscmulj (vector dynamic scaling complex conjugate multiply)
vdsmacini(vector dynamic scaling MAC initialization)
vdscmac(vector dynamic scaling complex MAC)
vdscmacj(vector dynamic scaling complex conjugate MAC)
vdscmaco(vector dynamic scaling complex MAC final result output)
vdsredsumn(vector dynamic scaling reduced sum for each n element)
vdscredsum(vector dynamic scaling complex reduced sum)
vredmaxi(vector reduced max with index)
vredmini(vector reduced max with index)
vlnlp(vector load nonlinear parameter)
vnle(vector non-linear exponent calculation instruction)
vnlm(vector non-linear mantissa calculation instruction)

## Slide 7
SC16
SC16
Zvw VS. RVV1.0 -- Conjugate Complex multiply
SC16
SC16
SC16
SC16
A0
A1
A2
A29
A30
A31
A1, A2 ... A31
vsetvl (SEW = 32bit LMUL=1)
vle32.v %[A], (%[Aaddr])
vle32.v %[B], (%[Baddr])
vdscmulj.vv %[C], %[A], %[B]
Zvw 4 Inst.
vsetvl (SEW = 16bit LMUL=1)
vlm.v v0, (%[imageMaskAddr])
vmv.i %[zero], 0
vle16.v %[A], (%[Aaddr])
vle16.v %[B], (%[Baddr])
vmul.vi %[B], %[B], -1, v0
vmerge. vvm %[Aimage], %[zeor], %[A], v0
vmerge. vim %[Areal], %[A], %[zero], v0
slidedown. vi %[Aimage], %[Aimage], 1
vmerge. vvm %[Bimage], %[zeor], %[B], v0
vmerge. vim %[Breal], %[B], %[zero], v0
slidedown. vi %[Bimage], %[Bimage], 1
vmul.vv %[real1], %[Areal], %[Breal]
vmul.vv %[real2], %[Aimage], %[Bimage]
vmul.vv %[image1], %[Areal], %[Bimage]
vmul.vv %[image2], %[Aimage], %[Breal]
vadd.vv %[real], %[real1], %[real2]
vadd.vv %[image], %[image1], %[image2]
slideup.vi %[image], %[image], 1
vmerge. vvm %[result], %[image], %[real], v0
RVV 1.0 20 Inst.
Zvw is 5X more efficient in codesize, efficency and power in this case.
SC16
SC16
SC16
SC16
SC16
SC16
B0*
B1*
B2*
B29*
B30*
B31*
B1*, B2* ... B31*

## Slide 8
Zvw VS. RVV1.0 -- Complex dynamic scaling MAC
SC16
SC16
SC16
SC16
SC16
SC16
A0
A1
A2
A61
A62
A63
A1, A2 ... A31
SC16
SC16
SC16
SC16
SC16
SC16
B0*
B1*
B2*
B61*
B62*
B63*
B1*, B2* ... B31*
vsetvl (SEW = 32bit LMUL=2)
vdsmacini. s %[AntShift]
vle32.v %[cir0], (%[cir0Addr])
vle32.v %[cir1], (%[cir1Addr])
vdscmacj.vv %[cir0], %[cir1]
vdscmaco.v %[cirSum]
vdscredsum.v %[result], %[cirSum]
Zvw 7 Inst.
vsetvl (SEW = 16bit LMUL=2)
vlm.v v0, (%[imageMaskAddr])
vmv.i %[zero], 0
vmv.v %[accReal], %[zero]
vmv.v %[accImage], %[zero]
vle16.v %[A], (%[Aaddr])
vle16.v %[B], (%[Baddr])
vmerge. vvm %[Aimage], %[zeor], %[A], v0
vmerge. vim %[Areal], %[A], %[zero], v0
slidedown. vi %[Aimage], %[Aimage], 1
vmerge. vvm %[Bimage], %[zeor], %[B], v0
vmerge. vim %[Breal], %[B], %[zero], v0
slidedown. vi %[Bimage], %[Bimage], 1
vwmac.vv %[accReal], %[Areal], %[Breal]
vwmac.vv %[accReal], %[Aimage], %[Bimage]
vwmac.vv %[accImage], %[Areal], %[Bimage]
vwmac.vv %[accImage], %[Aimage], %[Breal]
vsetvl (SEW = 32bit LMUL=1)
vsra.vv %[accReal], %[accReal], %[AntShift]
vsra.vv %[accImage], %[accImage], %[AntShift]
vsetvl (SEW = 16bit LMUL=1)
slideup. vi %[accImage], %[accImage], 1
vmerge. vvm %[result], %[accImage], %[accReal], v0
RVV 1.0 23 Inst.
Zvw is 3.5X more efficient in codesize, efficency and power in this case. Accuracy is another advantage.

## Slide 9
SC16
SC16
SC16
SC16
SC16
SC16
SC16
SC16
SC16
SC16
Zvw VS. RVV1.0 -- wideband average power
SC16
SC16
SC16
SC16
SC16
SC16
SC16
SC16
A0
A1
A2
A29
A30
A31
SC16
SC16
SC16
SC16
SC16
SC16
A1, A2 ... A31
A1H
A2H
...
A31H
A0
A1
A2
A29
A30
A31
Each A vector has different gain shift
vsetvl (SEW = 32bit LMUL=1)
vdsmacini.v %[gainShift]
vle32.v %[a0], (%[a0Addr])
vdsmacj.vv %[a0], %[a0]
vle32.v %[a1], (%[a1Addr])
vdscmacj.vv %[a1], %[a1]
vdscmacor.v %[acc]
vdscredsum.v %[sum32]
sum32[0] is the final result of SC16
Zvw 8 Inst.
A = [a0, a1]
vsetvl (SEW = 16bit LMUL=2)
vmv.v.i %[acc], 0
vmv.v.v %[gainShift2], %[gainShift]
vsetvl (SEW = 16bit LMUL=1)
vle16.v %[a0], (%[a0Addr])
vwmul.vv %[a0], %[a0], %[a0]
vle16.v %[a1], (%[a1Addr])
vwmacc.vv %[acc], %[a1], %[a1]
vsetvl (SEW = 16bit LMUL=2)
vsra.vv %[a0], %[a0], %[gainShift] // lost accuracy here
vsra.vv %[a1], %[a1], %[gainShift] // lost accuracy here
vadd %[a0], %[a0], %[a1]
vsra.vi %[a0], %[a0], n // output fixpoint format
vredsum.vs %[sum32], %[a0], %[acc]
sum32[0] is the final result of SC16
RVV 1.0 14 Inst.
Zvw is 2X more efficient in codesize, efficency and power in this case. Accuracy is another advantage.

## Slide 10
Zvw encoding space

## Slide 11
Zvw encoding space

## Slide 12
Zvw encoding space